## Slide 1: Aerial Pathfinding Reconnaissance Status Update
Jason Gilman, Max Griffith, Mark Johnson, Dilanka Weerasinghe

## Slide 2: Overview
Goal: Use aerial drone footage to find a safe path for a land vehicle.
Team Members and Responsibilities:
Dilanka Weerasinghe (Data Collection & Drone Control)
  Automated drone control and collection of aerial footage
Mark Johnson (Computer Vision & Mapping)
  Production of an obstacle map from drone videos
Max Griffith (Pathfinding & Drone Detection)
  Determination of vehicle starting location and route
Jason Gilman (Device Networking & UI)
  Creation of user interface and network interconnect
System Block Diagram

## Slide 3: Data Collection & Drone Control
Stages Complete:
Stand alone electronics
  Programmed individually and working
  Preboard header for sensors working with all sensors.
  PiCam records interval video and records to a datasheet with video name and time; working on gathering location data from the drone.
Drone
  Drone simulator Running
  Program will arm drone and perform safety check
  Can monitor drone SITL at time intervals
Stages Remaining:
Fix simulation issues with GPS location
Mount sensors to the drone
Integrate data collection into Waypoint program.

## Slide 4: Computer Vision & Mapping
Stages Complete:
Moving Object Removal
  Working as intended.
Image Stitching
  Requires more data points than we want to take.
  Workaround: Leverage assumptions about the path.
Depth Map Inference
  Likely need to tweak parameters depending on data.
  Workaround: Provide user an interactive way to do so.
Stages Remaining:
Depth Map Stitching
  Most important (and difficult) stage of the pipeline
Gradient Field Derivation
Obstacle Delineation
Demo: Moving Object Removal
Input Video
Output Image
Input Image (Left Eye View)
Output Depth Map
Demo: Depth Map Inference

## Slide 5: Pathfinding & Drone Detection
Stages Complete:
Finding straightforward path
  Working as intended
  Paths not taken for final path are marked as invalid (0)
Edge cases and error handling
  Edge cases such as finding cycles have been fixed (infinite loops)
  Errors such as invalid start/end locations and impossible paths
Stages Remaining:
Program movement of drone
  Giving instructions to the drone to follow
Programming drone path from a map input
  Bulk of project, formatting the map input for the algorithm
    This means creating a new "pixel" of size drone dimension from an area of map pixels
Cyclic Path:
Cyclic Path Solved*:
*The starting location is [0,0] and the ending location is [3,6]

## Slide 6: Device Networking & UI
Stages Complete:
Desktop application architecture and UI logic
  React Front-end compiled into .exe format
  Python Back-end for serving assets and software analysis functions
  User input standardization, error handling, and status updates for each stage of the system
Area of operation mapping functionality
  User plots area to be mapped by the aerial drone
  Creates navigation instructions for aerial drone using Lat-Lng-Elevation waypoints
Stages Remaining:
Implement server architecture on aerial and land drones
Establish communication between desktop app and drones
Mapping functionality: invalid area
Mapping functionality: valid area

## Slide 7
Execution Plan

## Slide 8
Validation Plan

## Slide 9
Data Collection & Drone Control
Hardware and software components are working well individually.
Future tasks are largely focused on in-subsystem integration and testing.
Computer Vision & Mapping
Depth inferencing is complete, and about as accurate as we hoped.
Greatest challenge ahead is merging depth maps of path sections.
Pathfinding & Drone Detection
Algorithm and edge cases completed for drone pathing
Next steps are to program drone without a map input and then with a map input.
Device Networking & UI
UI design and functionality completed
Next steps are to establish communication between desktop app and drones.
Key Takeaways

## Slide 10: Questions?